## Slide 1
Particles as surfactants and antifoams
N. D. Denkov and S. Tcholakova
Department of Chemical Engineering,
Faculty of Chemistry, Sofia University, Sofia, Bulgaria
Discussion at COST D43 Training School “Fluids and Solid Interfaces” Sofia, Bulgaria, 12–15 April, 2011

## Slide 2
Problem 1
Energy of particle adsorption

## Slide 3
    Particle adsorption energy = - a212(1-cos)2
a, nm | EA, J | EA/kT
1 | - 9.410-20 | - 23
10 | - 9.410-18 | - 2300
100 | - 9.410-16 | -230000
12 = 30 mN/m;  = 90 
EDIS
ER1-2

## Slide 4
Adsorption energy vs particle size
    EA>> kBT for a > 1 nm
12 = 30 mN/m;  = 90 

## Slide 5
Adsorption energy for particles with different contact angles
, deg | ER1-2/kT | EDIS/kT | EA/kT | EA, J
10 | 68.78 | -69.28 | - 0.5 | - 2.210-21
90 | 0 | -2300 | - 2300 | - 9.410-18
150 | -7430 | -575 | -8005 | - 3.310-17
12 = 30 mN/m; a = 10 nm

## Slide 6
Adsorption energy vs contact angle
12 = 30 mN/m; a = 10 nm
    Significant effect of contact angle on the energy of adsorption !

## Slide 7
Desorption energy
    Desorption is favored into the phase which wets better the particle!

## Slide 8
Desorption energy vs contact angle
, deg | ED, J | ED/kT
10 | 2.210-21 | 0.5
90 | 9.410-18 | 2300
150 | 1.610-19 | 41
12 = 30 mN/m; a = 10 nm

## Slide 9
Desorption energy vs contact angle
12 = 30 mN/m; a = 10 nm
    Maximum ED at cos = 0   = 90

## Slide 10
Problem 2
Interfacial tension of particle adsorption monolayers
Ideal 2-dimensional gas
Dilute adsorption layer
Low surface coverage
Gibbs isotherm
Surface coverage

## Slide 11
Surface tension at 30 % surface coverage
Close packing of particles on interface
 | Amin, nm2 | , molec./m2 | , molec./m2 | , mN/m
Surfactant | 0.4 | 2.51018 | 0.751018 | 69
Particle (10 nm) | 346.4 | 2.71015 | 8.21014 | 72

## Slide 12
Volmer adsorption isotherm
Surface tension at 80 % surface coverage
 | Amin, nm2 | , molec./m2 | , mN/m
Surfactant | 0.4 | 2.51018 | 31
Particle (10 nm) | 346.4 | 2.71015 | 72
    Particles are very inefficient at reducing surface tension even at very high surface coverage

## Slide 13
Problem 3
Formation of complete monolayer
Volume fraction
Specific surface area
 | ADR | VD | S
Monodisperse |  |  | 
Polydisperse |  |  | 
Mean volume surface radius

## Slide 14
Formation of complete adsorption layer
Close packing of particles on interface
Number of particles
Volume of particles
Particles required to cover the specific drop surface area
Mass of particles

## Slide 15
Particles in continuous phase
Particles in dispersed phase
Concentration of the particles

## Slide 16
Particles in continuous phase
P = C = 1 g/ml
a = 30 nm
R32 = 1 m
Particles
Surfactant
    25 times lower C are sufficient to cover the same drop area by surfactant molecules,   1.5 mg/m2

## Slide 17
Problem 4
Pressure for rupturing film stabilized by particle monolayer

## Slide 18
Capillary pressure vs film thickness
    The maximal pressure at h = 0
     the critical capillary pressure for film rupturing

## Slide 19
Critical capillary pressure vs contact angle
    Critical pressure decreases with increasing of contact angle and with increasing the distance between particles

## Slide 20
Optimal contact angle for film stability
Desorption energy
Critical pressure
12 = 30 mN/m
a = 10 nm
30    80
ED > 40 kT (irreversible adsorbed)
PCMAX > 0.7 MPa (b/a = 1.5)
Very high critical capillary pressure !

## Slide 21
Destabilization of films
Particles can aggregate on the surface and forming empty regions in the film.
The stability is much lower !

## Slide 22
Thank you for your attention !